## Slide 1
MODULE 01
Plumbing Terms & Definitions
The 40 vocabulary words that show up most often on Texas plumbing exams — defined in plain English with field examples.
TX Plumbing Exam Coach · Educational use only

## Slide 2
SECTION 1
Foundational terms — drainage system
Soil pipe — carries discharge from water closets and similar fixtures, with or without other discharge.
Waste pipe — carries discharge from fixtures other than water closets.
Stack — any vertical line of soil, waste, or vent piping extending through one or more stories.
Branch — any part of the piping system other than a main, riser, or stack.
Developed length — measured along the centerline of the pipe and fittings.
01 · Terms & Definitions
2 / 7

## Slide 3
SECTION 2
Trap vs. Vent — don't confuse them
Trap
A fitting that holds a water seal.
Seal: 2" minimum, 4" maximum (typical).
Prevents sewer gas from entering the building.
Every fixture needs one (except integral-trap WCs).
Vent
A pipe providing air circulation.
Protects the trap seal from siphonage and back-pressure.
Terminates in open air above the roof.
Sized from the fixture-unit load it serves.
01 · Terms & Definitions
3 / 7

## Slide 4
SECTION 3
Pressure & flow vocabulary
Static pressure — pressure at no flow.
Residual pressure — pressure remaining at the fixture during flow.
Friction loss — pressure drop due to flow through pipe and fittings.
Water hammer — surge caused by sudden stoppage of flow.
Cross-connection — any actual or potential connection between potable and non-potable.
01 · Terms & Definitions
4 / 7

## Slide 5
SECTION 4
Numbers you must memorize
2"
MIN TRAP SEAL
Standard fixture trap; protects against siphonage.
1/4"
PER FOOT
Minimum slope for 2½" and smaller horizontal drains.
80°F
MAX HOT
Where scald protection applies (typ. tub/shower).
Memorize these — they show up on almost every exam.
01 · Terms & Definitions
5 / 7

## Slide 6
CHECK
Knowledge Check
Which best defines 'developed length'?
A. Straight-line distance between two fittings
B. Total length measured along the centerline of pipe and fittings
C. Vertical rise only
D. Length of pipe minus fitting allowances
Answer: B — Developed length follows the pipe path, including fittings.
01 · Terms & Definitions
6 / 7

## Slide 7
Keep flowing.
01 · Terms & Definitions
Review · Drill · Pass. TX Plumbing Exam Coach
Educational and exam-prep use only. Not an official TSBPE product or legal substitute for adopted plumbing codes.