## Slide 1
MODULE 05
Backflow & Cross-Connection
Air gaps, RPZs, DCVAs, PVBs, AVBs — which device, which hazard, which location.
TX Plumbing Exam Coach · Educational use only

## Slide 2
CONCEPTS
What backflow really is
Backflow = reverse flow of water (or other liquids) into the potable supply.
Backsiphonage — caused by negative pressure upstream (water main break, fire flow).
Backpressure — downstream pressure exceeds supply pressure (booster pumps, boilers).
Cross-connection — any point where the two could meet.
05 · Backflow Protection
2 / 7

## Slide 3
HAZARD LEVEL
Match device to risk
High hazard (health)
Air gap — best protection, no moving parts.
RPZ — Reduced-Pressure Zone, both back-siphonage & back-pressure.
Required for irrigation w/ chemicals, hospitals, labs.
Low hazard (non-health)
DCVA — Double Check Valve, low hazard, both directions.
PVB — Pressure Vacuum Breaker, back-siphonage only.
AVB — Atmospheric Vacuum Breaker, simplest, no shutoff downstream.
05 · Backflow Protection
3 / 7

## Slide 4
AIR GAP
Physical separation rules
2×
DIAMETER
Min air gap = 2× the supply pipe diameter.
1"
MIN
Never less than 1 inch, regardless of pipe size.
3×
NEAR WALL
If within one pipe-diameter of a sidewall.
05 · Backflow Protection
4 / 7

## Slide 5
INSTALLATION
Common mistakes inspectors catch
RPZ installed below grade — must be above grade, accessible.
PVB installed lower than the highest downstream outlet (must be at least 12" above).
AVB with a shutoff valve downstream (never allowed).
No annual test record on file — required by TCEQ for testable devices.
05 · Backflow Protection
5 / 7

## Slide 6
CHECK
Knowledge Check
Which device protects against both back-siphonage AND back-pressure on a high-hazard cross-connection?
A. AVB
B. PVB
C. DCVA
D. RPZ
Answer: D — RPZ is the only listed device for high-hazard, both-direction protection.
05 · Backflow Protection
6 / 7

## Slide 7
Keep flowing.
05 · Backflow Protection
Review · Drill · Pass. TX Plumbing Exam Coach
Educational and exam-prep use only. Not an official TSBPE product or legal substitute for adopted plumbing codes.